## Cleaning your CPAP mask cushion, frame & headgear

#### Daily cleaning tips:

  - Unplug your CPAP machine from the power source.

  - Disconnect the mask and air tubing from the CPAP machine.

  - Disassemble your mask into 3 parts (headgear, cushion and frame).

  - In a sink or tub, clean your mask cushion and headgear to remove any oils.

  - Gently rub with MILD soap (BABY SHAMPOO)  and warm, DISTILLED water

.

  - Avoid using stronger cleaning products, including dish detergents, as they may damage the mask or leave harmful residue.

  - Rinse again thoroughly with warm, DISTILLED water.

  - Place the cushion and frame on a flat surface, on top of a towel, to dry.

  - Avoid placing them in direct sunlight.

## Air tubing cleaning tips

#### Weekly cleaning tips:

- Unplug your CPAP machine from the power source.

- Disconnect the air tubing/hose from your mask and CPAP machine.

- In a sink or tub, rinse the inside and outside of the air tubing with mild soap(BABY SHAMPOO) and warm, DISTILLED water. Avoid using stronger cleaning products, including dish detergents, as they may damage the air tubing or leave harmful residue.

- Rinse again thoroughly with warm, DISTILLED water.

- Place the air tubing on a flat surface, on top of a towel, to dry. Avoid placing in direct sunlight.

## Humidifier tub cleaning tips

### Daily cleaning tips:

- Unplug your CPAP machine from the power source.

- Disconnect the humidifier tub from the CPAP machine.

- In a sink or tub, rinse the humidifier tub with mild soap (BABY SHAMPOO) and warm, DISTILLED water. Avoid using stronger cleaning products, including dish detergents, as they may damage the humidifier tub or leave harmful residue.

- Rinse again thoroughly with warm, DISTILLED water.

- Place the humidifier tub on a flat surface, on top of a towel, to dry. Avoid placing in direct sunlight.

- The humidifier tub should always be clean, clear and free of discoloration.

### Weekly cleaning tips:

- Once a week, soak your humidifier tub in a solution of 1-part white vinegar and 1-part water for 15-20 minutes.

- After soaking, rinse thoroughly with warm, DISTILLED water.

- Place the humidifier tub on a flat surface, on top of a towel, to dry.

- Avoid placing in direct sunlight.